## Slide 1: AVNRT
Atrioventricular Nodal Reentry Tachycardia

## Slide 2: PATIENT IN AVNRT: EKG
Micro reentry circuit
Paroxysmal
Must have a slow and a fast pathway
EKG - P Wave closely coupled after QRS (or inside QRS) because the circuit is going down the slow pathway and up the fast pathway

## Slide 3: AH JUMP
Decremental conduction
Indication of slow pathway
50+ ms prolongation in AH with 10 ms shortening of S2

## Slide 4: ECHO BEATS
AV Nodal Echo – one journey of re-entrance
  Pulsing the HRA (Programmed Stimulation)
AVNRT is usually characterized by several of these beats

## Slide 5: PATIENT IN AVNRT: EMG
Characterized by several echo beats
This patient will be diagnosed with AVNRT.

## Slide 6: AVNRT CONDUTION
Down the slow pathway, up the fast pathway
Slow pathway - fast refractory
Fast pathway - slow refractory

## Slide 7: ABLATION
Target: slow pathway
  Small and sensitive area
  Burning inferior and posterior to the AV node; very close to the His
  Stop ablation if an A signal is seen without a V – sign of heart block
Successful when there is no tachycardia induction
  No echo beats, no AH jump
  Wenckebach cycle length longer

## Slide 8
Thank you!